Alsa Modular Synth
Y. collette (ycollette.nospam@free.fr)
https://audinux.github.io

---
Modular synthesis
http://www.idreamofwires.org/
A good documentary about modular synthesis

---
AMS
http://alsamodular.sourceforge.net/

---
A simple patch
MCV: Midi Controlled Voltage
VCO: Voltage controlled oscillator
Approx: adsr envelope
VCA: Voltage controlled amplifier
The gate output of the MCV = 1 when a key was supported and 0 otherwise. The FREQ output contains the frequency of the MIDI note played.
The VCA is there to gradually play the note via an ADSR envelope (otherwise we hear a click).
PCM OUT: Audio output

---
A MIDI Patch with controller
Advanced MCV: Midi Controlled Voltage Module to recover controller values
Amplifier: allows you to add a gain to the value of the controller
Lin VCA: allows you to modulate the amplitude of the signal by the value of the controller

---
Patch mixing MIDI and audio

---
Preset management
We select a parameter.
We click on this button.
A configuration window is gradually built for the patch
View → Control center
View → Settings view